## Slide 1: Introduction to Data & Advanced Programming Blocks
ROBOTICS II
Module 1

## Slide 2: Objectives
Identify the programming palettes on the NXT software interface.
Explain the function of data and advanced block commands
Use the NXT software to program simple tasks using data and advanced block commands

## Slide 3: Introduction
Robots perform a wide variety of important jobs.
For example, robots explore other planets, investigate deep-sea volcanoes, assemble automobiles, and perform surgery.

## Slide 4: Examples

## Slide 5: Programming Palettes
Common Palette
Complete Palette
Custom Palette

## Slide 6: Common Palette
has the most commonly used blocks, giving you quick access to the blocks that you’ll use most frequently.

## Slide 7: Complete Palette
includes all the available blocks, including the ones on the Common Palette

## Slide 8: Custom Palette
includes blocks that you create or downloaded from the Internet

## Slide 9: Activities 1 ,2 & 3 on pages 4 -5

## Slide 10: Data Programming Blocks
Data Programming Blocks are used to set up Boolean logic, random conditions, ranges and threshold for sensors, logical comparisons, creating variables and constants.
Data Blocks

## Slide 11: Logic Block
Logic Block: The Logic Block lets you combine multiple conditions, allowing your program to make more complex decisions. This lets your program ask questions like “Is the Touch Sensor pressed and the Light Sensor reading greater than 50?”

## Slide 12: Math Block
Math Block: The Math Block is used to perform any calculation your program needs. You can use the math block to calculate the distance your robot is moving and the total score for a basketball machine.

## Slide 13: Compare Block
Compare Block: The Compare Block allows you to compare any two numbers, giving you more flexibility than using a Switch or Loop block alone. For example, you can compare the readings from two Rotation Sensors. You can then use the result of the comparison to control a Switch or Loop block.

## Slide 14: Range Block
Range Block: The Range Block determines whether a number is inside or outside a range of numbers. There are two questions you can ask using the Range block: “Is the test value inside the range (between the lower and upper limits)?” and “Is the test value outside the range (less than the lower limit or greater than the upper limit)?”

## Slide 15: Random Block
Random Block: The Random Block is used to generate a random number. You can use this block to create robotic games or to add some randomness to your robot’s behavior. Often a robot that is a little unpredictable can be more interesting or seem to have more personality.

## Slide 16: Variable Block
Variable Block: The variable Block stores and retrieves variable values. You can save sensor readings in a variable and then update them after performing mathematical values.

## Slide 17: Constant Block
Constant Block: Constant Block is used to access constants in your program. This block looks like the Variable block, with a lock added to show that the value cannot be changed.

## Slide 18: Advanced Programming Blocks
Advanced Programming Blocks are used to add text, convert data to text, control the sleep function of the NXT, save files on the NXT, calibrate sensors, and reset motors.
Advanced Block

## Slide 19: Number To Text Block
The Number to Text Block converts a number to its equivalent text data. You can use this block to convert the sensor readings to a text that can then be displayed on the NXT screen.

## Slide 20
The Text Block lets you join together up to three pieces of text, which can be useful for adding labels to values you display on the NXT’s screen.
Text Block

## Slide 21
The Keep Alive Block lets you prevent the NXT from turning itself off. The icon for this block is a pair of Zs (to indicate sleeping) crossed out using a red circle with a line through it. Having the NXT go to sleep is useful for saving your batteries; however, you may want to prevent the NXT from turning off while your program is running. That’s where the Keep Alive block comes in.
Keep Alive Block

## Slide 22
The File Access Block allows you to create your own files on the NXT, which you can use to store any data that your programs use. The information you store in a file is persistent, meaning that it’s still available after your program ends, even if you turn off the NXT.
File Access Block

## Slide 23
The Calibrate Block is used to calibrate light and sound sensors by adjusting the minimum and maximum values of the sensor.
Calibrate Block

## Slide 24
The Reset Motor Block resets the adjustment value of the motor to zero .
Reset Motors

## Slide 25
LAB ACTIVITY 1

## Slide 26
LAB ACTIVITY 2

## Slide 27
REVIEW QUESTIONS (MODULE)

## Slide 28
APPENDIX I – EXPLORER ROBOT BUILDING GUIDE.